## Slide 1: HPR Staging & Air Starting By Gary Stroick
Complex Rocket Design Considerations

## Slide 2: Agenda
Tripoli Safety Code
Technical Considerations
Clusters/Air Starts
Staging
Summary

## Slide 3: Tripoli Complex Project Safety Code
Complex High Power Rocket. A high power rocket that is multi-staged or propelled by a cluster of rocket motors intended for simultaneous ignition at launch or in the air.
Stability. A person intending to operate a high power rocket shall determine its stability before flight. This person shall provide documentation of the location of the center of pressure and the center of gravity of the high power rocket to the RSO if the RSO requests same.
A person shall not be closer to the launch of a high power rocket than the applicable minimum safe distance set forth in the Safe Distance Table.
Minimum Safe Distance Table |  |  | 
Installed Total Impulse (N-sec) | Equivalent Motor Type | Minimum Distance Commercial (feet/meter) | Minimum Distance Research (feet/meter)
160.01 – 320.00 | H | 200/61 | 250/76
320.01 – 640.00 | I | 200/61 | 250/76
640.01 – 1,280.00 | J | 200/61 | 250/76
1,280.01 – 2,560.00 | K | 300/91 | 350/96
2,560.01 – 5,120.00 | L | 500/152 | 500/152
5,120.01 – 10,240.00 | M | 1,000/305 | 1,000/305
10,240.01 – 20,480.00 | N | 1,500/457 | 1,500/457
20,480.01 – 40,960.00 | O | 2,000/610 | 2,000/610
40,960.01 – 890,000.00 | P-T | N/A | 2,500/762

## Slide 4: General Technical Considerations
Motor Selection (Air Start, Cluster or Multi Stage)
  Propellant Type
    Avoid Hard Starting Motors (e.g. Greens)!
    AeroTech
      Blue Thunder
      White Lightning
    Cesaroni
      Black pellet design permits use of all propellant types (54mm)
  Core Size
    Smaller is Better (e.g. usually implies easier starting)

## Slide 5: General Technical Considerations
Igniter/E-Match Selection & Wiring (Air Start or Multi Stage)
    Low Amp, High Temp & Large Gas Production Igniters (E=IR)
      Commercially made: 1) Oxral (5A), 2) J-Tek (9A - calculated)
      Commercial kits: 1) Firestar (8.64A), 2) Magnelite (11.25A)
    Battery Requirements
      Igniter battery separate from altimeter
      Wire igniter batteries in parallel
    Ignition
      Support - Wood dowel/Plastic tube/Thread
      Roughing Core/Pyrogen Coat/Propellant Slivers
      Research only – Head End Ignition
    Premature Ignition
      Battery Reversal
      RF Transmissions
      To shunt or not to shunt
9 Volts
2 x Amperage
(1,160 mAh
for Duracell)
      Recommendation: Test on motors in sustainers before Air Starting or Staging

## Slide 6: Staging
Why?
Design Considerations
Simulation Techniques
Altimeter Requirements & Programming
Launch Preparation

## Slide 7: Why Stage?
Additional set of challenges at current cert. level
  Multiple flight profiles
  Multiple deployments
  Combined and individual stability profiles
  Combination of multiple motor types
  Construction challenges
    Sustainer/Booster coupling
    Electronics driven ignition

## Slide 8: What can go Wrong?
Failure Modes (non-exhaustive)
  Stage ignition failure
  Late stage ignition
  Coupler malfunction
  Early, late or no deployment
Resultant Flight Profile
  Non-vertical flight (horizontal, loops, powered descent, …)
  Coupler Failure Issues (Tolerance, Strength, …)
  Shred
  Deployment issues
    Motor ignition after parachute deployment
    Parachute deployment during motor burn
    Zippering
    Stripping parachute
    Negative Altitude Records (i.e., Core Sampling )
  Estimated altitude not reached

## Slide 9: Staging – Design Considerations
Inline Staging (Single Sustainer)
  Vertically stacked boosters and sustainer
  Each booster is discarded after motor burnout
Parallel Staging (Single Sustainer)
  Similar to Air Starting
  Boosters are externally attached to the sustainer
  Each booster separates from the sustainer after its motor burns out
Parasite Staging (Multiple Sustainers)
  Similar to Air Starting
  Sustainers are externally attached to the booster
  Each sustainer separates after booster burn out

## Slide 10: Staging – Configurations
Inline (e.g. Falcon 9)
  2 or more stacked stages (usually not more than 3 stages)
  Direct ignition is not feasible with APCP motors
Construction - Interstage Couplers
  Rod or coupling tube design
  Electronics may perform the following functions:
    Ignition of next stage
    Recovery deployment for prior stage
    Charge separation of stages
Separation - Booster
  Drag, thrust, or charge separation of stages
  Upper stage ignition delays (coasting to obtain higher altitudes)
    Consider igniter firing time and time for motor pressurization
    Coasting too long can result in reduced altitudes, non-vertical flights, …
    Recommend to start initially with no delay after booster burnout
Static/Dynamic Stability
  All flight configurations must be stable which includes individual boosters, sustainer, and all design combinations
    Caveat: slow subsonic boosters could tumble but may cause recovery issues
Electronics

## Slide 11: Staging – Configurations
Parallel (e.g., Delta II)
  2 or more external boosters
  Boosters ignited with sustainer, before, after, or any permutation
Construction - Booster Mounting to Sustainer
  Aft support options
    Guides with a pivot rod and notched guides on sustainer
    Explosive bolts
  Fore support options
    Slotted booster with guides and pivot rod, sustainer hook
    Explosive bolts
  Electronics may perform the following functions:
    Booster separation and recovery deployment
    Sustainer ignition and recovery deployment
Separation - Booster
  Charge or ejection separation of boosters
  Separate electronics activation
Static/Dynamic Stability
  Again sustainer with all booster flight configurations must be stable
      Angle boosters through CG when possible
Booster
Sustainer

## Slide 12: Staging – Configurations
Parasite (e.g., Space Shuttle kind of)
  2 or more sustainers
  Sustainers ignited after booster burn out
Construction – Sustainer mounting to booster
  Aft support option
    Booster has notched supports for sustainer fins
  Fore support option
    Booster fitting for sustainer launch lug or rail guide
  Electronics may perform the following functions:
    Sustainer ignition, separation and recovery deployment
    Booster recovery deployment
Separation - Sustainer
  Thrust or charge separation
Static/Dynamic Stability
  Again booster with all sustainer flight configurations must be stable

## Slide 13: Staging – Simulation Techniques (Rocksim v9.1.1)
‘Rocket design attributes’ tab
  Set ‘Number of stages:’ field (default is one)
    Use one for Parallel or Parasite designs
    Use two or more for Inline designs
‘Rocket design components’ tab
  Components
    Sustainer (Uppermost stage)
    Inline
      Booster or Booster 1 (1st stage)
      Booster 2 (2nd stage)
      Design and build each stage
        There must be at least one motor mount per stage
    Parallel & Parasite
      Add one Pod per Booster/Sustainer, name each booster group, leave ejected during simulations box checked, and set radial position
      Select Pod and build Booster/Sustainer with a motor mount

## Slide 14: Staging – Simulation Techniques (Rocksim v9.1.1)
Load Motors using ‘Prepare to Launch’ dialog box ‘Engine Selection’ tab
  Inline Simulation
    Load motors with appropriate Ignition Delay (coast time)
    Booster motors must have a non-negative numeric Ejection Delay value to stage (Stage Separation Time)
    All motors will be ignited in stage sequence
  Parallel Simulation
    Load Booster & Sustainer motors with appropriate Ejection and Ignition Delays
    Use identical Ejection Delay times for all motors that are Boosting simultaneously
    Booster separation occurs based on Ejection Delay (must have a non-negative numeric value)
    All Ignition Delay times are measured from 1st ignition (e.g., no tie to pods)
  Parasite Simulation (limited to one sustainer only!)
    Load Booster and Sustainer motors with appropriate Ejection and Ignition Delays
    Booster separation occurs based on Ejection Delay (must have a non-negative numeric value)
    All ignition delay times are measured from 1st ignition (e.g., no tie to pods)

## Slide 15: Staging – Altimeter Requirements
Minimum
Timer(s)
Pyro channel control based on:
  Multiple Timed Delays
Two or more pyro channels
Preferred
Accelerometer with timer
Pyro channel control based on:
  Deceleration Detection
  Timed Delay
  Recognition of Multiple Deceleration Events
Barometer (for dual deployment of main)
Two or more pyro channels
Tilt Detection

## Slide 16: Staging – Altimeter Programming
Detect Liftoff
For Each Stage X
  Do
    If Barometric Pressure Increasing or Vertical Velocity < 0 or Tilt > 10° then go to Deployment
  Until Decelerating Vertically And End of Stage X Time Delay
  Fire Stage X Igniter(s)
Next Stage
Deployment
  Wait Until Apogee Detected And End of Apogee Time Delay
  Fire Drogue/Main E-Match(es)

## Slide 17: Staging – Launch Preparations
Igniters
  Always wire in Parallel
  Consider dipping in pyrogen
Solid Fuel Motors
  Roughen top grain core
  Lightly coat top grain core with pyrogen

## Slide 18: Staging Summary
DO’s
Simulate your flight (all configurations)
Learn your altimeter and programming alternatives
Augment igniters and/or motors
Cant motor mounts through CG (if possible)
Use robust coupling and separation methods
Separate batteries for igniters and altimeters
Don’ts
Use hard starting motors or large core motors in sustainers
Wire igniters/e-matches in series
Use high amperage igniters

## Slide 19: Cluster/Air Starting
Why?
Design Considerations
Simulation Techniques
Altimeter Requirements & Programming
Launch Preparation

## Slide 20: Why Cluster or Air Start?
Cluster
  Additional set of challenges at current cert. level
    Igniting multiple motors simultaneously
    Combining multiple motor types
    Centering rings & motor mounts
Air Start
  All of the above plus
  Electronics driven ignitions
  Combine motors and delays for adjustable flight profile

## Slide 21: What can go Wrong?
Asymmetrical Thrust
  One or more motors do not ignite
  One or more motors ignite late
Resultant Flight Profile
  Non-vertical flight (angled flight, loops, …)
  Unstable due to inadequate thrust (wind cocking)
  Deployment issues
    Late (if motor ejection is used)
    Zippering
    Stripping parachute
  Estimated altitude not reached

## Slide 22: Clustering/Air Starting – Design Considerations
Motor Mounting
  Alignments
    Axially Parallel
      Unstable under Asymmetrical Thrust
    Angled through Center of Gravity
      Stable under Asymmetrical Thrust
  Motor Retention
    Spacing between mounts
  Layout Options
    Geometries must be balanced
    Heterogeneous mount sizes
Inline geometries will always require the largest diameter airframe

## Slide 23: Clustering/Air Starting - Geometries
Side by Side – Requires identical motors
  Not an option for Air Starting
Alternatives
  Triangle – Also requires identical motors and not an Air Starting option
  Inline – Outside motors must be identical may be used for Air Starting
Square – Motors opposite of center must be identical
  Up to two motor types may be used
  Up to one air start is possible
Star – Opposite motors must be identical
  Up to three motor types may be used
  Up to two air starts are possible
Hexagon – Opposite motors must be identical
  Six motor configuration (There is also a Rectangle Configuration)
    Up to three motor types may be used
    Up to two air starts are possible
  Seven motor configuration
    Up to four motor types may be used
    Up to three air starts are possible

## Slide 24: Clustering/Air Starting – Simulation Techniques (Rocksim v9.1.1)
Parallel Motor Mounts
  Add an Inside Tube, name it and mark as motor mount
  Add other components to the motor mount (engine block, …)
  If more motor tubes of this type are needed select Cluster
    For uniform mounts select the appropriate pattern and follow the Wizard instructions
    For non-uniform mounts select “User tube count & radius” option and follow the Wizard instructions
  Select a motor mount and add a centering ring
    The necessary holes are automatically added
    Copy the centering ring and reposition as many times as needed
Canted motor mounts cannot be simulated
  Copy needed motor files
  Reduce thrust curve using cosine of motor mount angle

## Slide 25: Clustering/Air Starting – Simulation Techniques (Rocksim v9.1.1)
Load Motors using ‘Prepare to Launch’ dialog box ‘Engine Selection’ tab
  Cluster Simulation
    Load motors with no Ignition Delay
    All motors will be ignited simultaneously
  Air Start Simulation
    Load motors with Ignition Delays (type value then must hit <enter key> - Rocksim quirk)
    Use identical Ignition Delay times for all motors that are Air Started simultaneously
    Use different Ignition Delay times for each set of Air Starts
    All Ignition Delay times are measured from 1st ignition

## Slide 26: Air Starting – Altimeter Requirements
Minimum
Timer(s)
Pyro channel control based on:
  Multiple Timed Delays
Two or more pyro channels
Preferred
Accelerometer with timer
Pyro channel control based on:
  Deceleration Detection
  Timed Delay
  Recognition of Multiple Deceleration Events
Barometer (for dual deployment of main)
Two or more pyro channels
Tilt Detection

## Slide 27: Clustering/Air Starting – Altimeter Programming
Detect Liftoff
For Each Air Start X
  Do
    If Barometric Pressure Increasing or Vertical Velocity < 0 or Tilt > 10° then go to Deployment
  Until Decelerating Vertically And End of Air Start X Time Delay
  Fire Air Start X Igniter(s)
Next Air Start
Deployment
  Wait Until Apogee Detected And End of Apogee Time Delay
  Fire Drogue/Main E-Match(es)

## Slide 28: Clustering/Air Starting – Launch Preparations
Igniters
  Always wire in Parallel
  Protect wires with Aluminum Tape
  Consider dipping in pyrogen
Solid Fuel Motors
  Roughen top grain core
  Lightly coat top grain core with pyrogen
Motor Mounts
  Cover empty mounts with Aluminum Tape

## Slide 29: Clustering/Air Starting Summary
Do’s
Protect igniter wiring
Design for motor retention
Cant motor mounts through CG
Simulate your flight
Learn your altimeter and programming alternatives
Augment igniters and/or motors
Separate batteries for igniters and altimeters
Don’ts
Use hard starting motors or large core motors
Wire igniters/e-matches in series
Use high amperage igniters

## Slide 30: Summary
Many aspects of Air Starting and Staging are similar
  Altimeter selection & programming
  Some design elements
  Motor and igniter preparation
Clustering, Air Starting & Staging provide new construction, electronics, and motor challenges at your current certification level
  Combine all three for even greater challenges